## Slide 1: FortiGate on Microsoft Azure
High availability and resiliency
Joeri Van Hoof – Piotr Nowotarski
Version 1.0

## Slide 2: High availability and resiliency
Single VM
Active Passive with UDR and PIP shifting
Active Passive with Standard Load Balancer
Active Active

## Slide 3: High availability and resiliency
Microsoft offers different SLA’s on the platform depending on the used technology.
  Single VM with Premium storage: 99.9%
  Availability Set (different rack and power): 99,95%
  Availability Zone (different datacenter in the same region: 99,99%
Maintenance to the hosts of the VM’s is performed from time to time.
  Microsoft provides you notifications when a reboot is required and a self-service time window when this reboot needs to happen. After this time window and no reboot happened, Microsoft will schedule this maintenance themselves.
  https://docs.microsoft.com/en-us/azure/virtual-machines/linux/maintenance-notifications
SLA offered by the platform
Notes: https://azure.microsoft.com/en-us/support/legal/sla/virtual-machines/v1_8/

## Slide 4: Azure resources information

## Slide 5: Public IP, private IP, public IP prefix
Private IP:
  Static or dynamic IP (don’t mix)
  Assigned from the subnet the network interface is deployed in
Public IP:
  SKU:
    Basic: Static or dynamic IP
    Standard: Static only
  Assigned by Microsoft, IPv4 or IPv6
Public IP prefix (Preview): a range of public IPv4 IP address
https://docs.microsoft.com/en-us/azure/virtual-network/virtual-network-ip-addresses-overview-arm
Notes: https://docs.microsoft.com/en-us/azure/load-balancer/load-balancer-ipv6-overview

## Slide 6: Azure Load Balancer
SKU:
  Basic Load Balancer:
    Free
  Standard Load Balancer
    First 5 rules + additional rules + Data processed
    HA Ports
Supported protocols: TCP and UDP (ICMP)
Health probe: TCP, HTTP and HTTPS
Outbound SNAT if no public IP on the network interface. Beware of limitations on the SNAT number of connections.
https://docs.microsoft.com/en-us/azure/load-balancer/load-balancer-overview
https://docs.microsoft.com/en-us/azure/load-balancer/load-balancer-outbound-connections
Notes: https://docs.microsoft.com/en-us/azure/load-balancer/load-balancer-ipv6-overview

## Slide 7: Single VM

## Slide 8: Single VM
Outbound:
  SNAT behind external interface public IP
Inbound:
  DNAT by Azure from external interface public IP to private IP. Then DNAT from private IP to VM IP. Source remains unchanged.
Internal:
  No NAT
Upgrades will cause disruption
SLA:
  99,9% w. Premium Storage
Virtual Network - VNET
Subnet External
Subnet Internal
Subnet backend 1
Subnet backend 2

## Slide 9: Active Passive with UDR and PIP shifting

## Slide 10: Active Passive
Virtual Network - VNET
Subnet External
Subnet Internal
Subnet backend 1
Subnet backend 2
Public IP
Attached to the active FortiGate
Subnet HA SYNC
Subnet HA MGMT
Notes: Outbound to internet:
-traffic to internet is broken after FW failover, session is lost and not reestablished
Inbound (DNAT)
-SSH session is broken after FW failover, session is lost and not reestablished
-SNAT is not needed in DNAT rule, backend server can see client real IP
-DNAT should be configured on WAN interface without IP, but with 0.0.0.0/0. Thanks to that DNAT will work on both firewalls, no matter which is active
East-West
-SSH session is broken after FW failover, session is lost and not reestablished
VPN traffic (Express route simulation)
-no SNAT needed, traffic can flow with original Ips
-during failover of Firewalls, Wget is frozen and after second box become active Wget continue to download the rest of the file. Session was not broken.
Cons:
-failover takes around 1minute
-
-MGMT on NIC4 needs to have access to Internet to update UDR and Public IP
-apart from VPN traffic all sessions are lost and need to be reestablished after failover
-a lot of manual work with UDR configuration in SDN configuration on Firewall
-6.0 OS supports only SDN connector to one subscription
-Firewall VM needs to have 4 NICs, expensive !
Pros
-customer can use lift & shift approach as configuration is simplier than with External and Internal LB in AA cluster
-simplier architecture than AA cluster

## Slide 11: Active Passive
Lift & Shift from on-premise
North-south traffic inspection
East-west traffic inspection
ExpressRoute traffic inspection
Site 2 Site VPN
Client 2 Site VPN
Use cases

## Slide 12: Active Passive
Deployment requires 4 NIC vm’s. A license supporting lower number of CPU’s can be used and will only use the number of CPU’s supported for the license
Failover time is undefined and ranges from 30sec to x min depending on the load of the Azure platform
Failover causes session to block. Basic public ip has slower failover times than the standard public ip
NIC 4 - MGMT ports needs internet access (route)
NIC 4 - MGMT ports needs a public IP for each VM when using Standard public IP’s
Standard public IP’s require a NSG (Any, Any, Allow minimum) on each subnet or interface to function
FortiOS 6.0.x: SDN Fabric Connector only supports one tenant, one subscription. All routes and public IP’s need to be in the same resource group as the firewall
FortiOS 6.2.x: Multiple SDN Fabric Connectors can be run to support multiple subscriptions and UDR
A lot of configuration of each UDR route to monitor in the SDN connector via CLI
On failure of changing adapting UDR routing or public ip change there is no auto-healing or revert.
Caveats
Notes: To test:
6.0.4 Failover does the SDN connector requires a resource group or not? It is not required for object retrieval but is it required for failover
6.2.0 Change UDR with same UDR name in different subscriptions

## Slide 13: No PIP attached to MGMT NIC4
Standard public IP’s only use static assigned IP’s. If you have no PIP on the MGMT NIC you will encounter the following issues:
  FortiGate is not able to reach Azure to update UDR and PIP, failover is not working.
  Same behaviour will happen if you forget to attach NSG to NIC4 as Standard SKU Public IP MUST have NSG attached to it to be able to go out to internet
Basic public IP’s support dynamic assignment. When no PIP is attached to the VM, a Basic PIP from the Azure IP pool is used.
Caveats
https://docs.microsoft.com/en-us/azure/virtual-network/virtual-network-ip-addresses-overview-arm

## Slide 14: No PIP attached to MGMT NIC4
To make Active/Passive setup more secure you can disable management ports on NIC4
  Attach it to port 2 and access it via S2S VPN, C2S VPN, Azure VPN Gateway or ExpressRoute
  Attach it to port 1 and provide public access with ACL and NSG restrictions to specific public IP’s
  https://docs.fortinet.com/document/fortigate/6.2.0/handbook/545196/local-in-policies
It has no influence on connectivity with Azure in terms of UDR, PIP or object updates. Whole setup works correctly in such configuration
Caveats

## Slide 15: Active Passive
F(S) : Standard_F4 and above
Fsv2: Standard_F8(s)_v2 and above
Supported Azure VM sizes
https://docs.fortinet.com/vm/azure/fortigate/6.2/azure-cookbook/6.2.0/271726/instance-type-support
Notes: https://docs.fortinet.com/vm/azure/fortigate/6.2/azure-cookbook/6.2.0/271726/instance-type-support

## Slide 16: Active Passive
Outbound (south - north):
  SNAT using external interface public IP if present or loadbalancer IP(‘s)
  Session is not recovering on FW failover
Inbound (north - south):
  DNAT by Azure from external interface public IP to private IP. Secondly DNAT using Virtual IP private IP to VM IP.
  SNAT not required. UDR send traffic back to the active unit
  Session is not recovering on FW failover
Internal (east – west):
  No NAT
  Session is not recovering on FW failover
Traffic flow

## Slide 17: Active Passive
Site-2-Site VPN
  No NAT
  UDR routes for the client network needs to be routed back to the active firewall
  IPSEC tunnel can be terminated on the public IP and terminated on the active firewall
  Upon failover the IPSEC VPN tunnel needs to reestablished to the passive firewall
Client-2-Site VPN
  No NAT
  UDR routes for the client network needs to be routed back to the active firewall
  VPN tunnel is terminated on the active firewall
ExpressRoute – Azure VPN Gateway
  No NAT
  UDR routes for the client network needs to be routed back to the active firewall
Traffic flow

## Slide 18: Active Passive
Fortinet documentation
  https://docs.fortinet.com/vm/azure/fortigate/6.2/azure-cookbook/6.2.0/651421/deploying-and-configuring-active-passive-ha
  https://docs.fortinet.com/vm/azure/fortigate/6.0/use-case-high-availability-for-fortigate-on-azure/6.0.0/651421/deploying-and-configuring-active-passive-ha
ARM Templates
  https://github.com/fortinetsolutions/Azure-Templates/tree/master/FortiGate/Active-Passive%20HA
  https://github.com/jvhoof/fortinet-azure-solutions/tree/master/FortiGate/QuickStart-AP
  Click here to deploy: https://portal.azure.com/#create/Microsoft.Template/uri/https%3A%2F%2Fraw.githubusercontent.com%2Fjvhoof%2Ffortinet-azure-solutions%2Fmaster%2FFortiGate%2FQuickStart-AP%2Fazuredeploy.json
Microsoft:
  https://docs.microsoft.com/en-us/azure/architecture/reference-architectures/dmz/nva-ha#pip-udr-nvas-without-snat
Resources

## Slide 19: Active Passive with Standard Load Balancer

## Slide 20: Active Passive with Azure Standard Load Balancer
Virtual Network - VNET
Subnet backend 1
Subnet backend 2
Public IP
Subnet External
Subnet Internal
Subnet HA SYNC
Subnet HA MGMT
Optional public IP
Optional public IP
Notes: Outbound to internet:
-traffic to internet is broken after FW failover, session is lost and not reestablished
Inbound (DNAT)
-SSH session is broken after FW failover, session is lost and not reestablished
-SNAT is not needed in dest NAT rule, backend server can see client real IP
-DNAT should be configured on WAN interface without IP, but with 0.0.0.0/0. Thanks to that DNAT will work on both firewalls, no matter which is active
East-West
-SSH session is broken after FW failover, session is lost and not reestablished
VPN traffic (Express route simulation)
-no SNAT needed, traffic can flow with original Ips
-during failover of Firewalls, Wget is frozen and after second box become active Wget continue to download the rest of the file. Session was not broken.
Cons:
-failover takes around 1minute
-
-MGMT on NIC4 needs to have access to Internet to update UDR and Public IP
-apart from VPN traffic all sessions are lost and need to be reestablished after failover
-a lot of manual work with UDR configuration in SDN configuration on Firewall
-6.0 OS supports only SDN connector to one subscription
-Firewall VM needs to have 4 NICs, expensive !
Pros
-customer can use lift & shift approach as configuration is simplier than with External and Internal LB in AA cluster
-simplier architecture than AA cluster

## Slide 21: Active Passive with Azure Standard Load Balancer
Lift & Shift from on-premise
North-south traffic inspection
East-west traffic inspection
ExpressRoute traffic inspection
Site 2 Site VPN
Client 2 Site VPN
Use cases

## Slide 22: Active Passive with Azure Standard Load Balancer
Deployment requires 4 NIC vm’s. A license supporting lower number of CPU’s can be used and will only use the number of CPU’s supported for the license
Failover time is defined by the failover detection of the Load Balancer. A probe fail time is 5 seconds and it has to fail 2 times. This results in a failover time of around 10-15 seconds
Failover causes north-south session to block
NIC 4 - MGMT ports need a public IP for each when using Standard public IP’s
Standard public IP’s require a NSG (Any, Any, Allow minimum) on each subnet or interface to function
SDN Fabric Connector can be used for dynamic address discovery
VPN Setup is more complex as the LB only support TCP/UDP (UDP 500 and UDP 4500) and no IKE. When using the optional public IP’s attached to the network interface the source IP of the IPSEC VPN will be different depending on the active firewall
Azure Load Balancer does not support ICMP, only TCP & UDP are supported
Caveats

## Slide 23: No PIP attached to MGMT NIC4
To make Active/Passive setup more secure you can disable management ports on NIC4
  Attach it to port 2 and access it via S2S VPN, C2S VPN, Azure VPN Gateway or ExpressRoute
  Attach it to port 1 and provide public access with ACL and NSG restrictions to specific public IP’s
It has no influence on connectivity with Azure in terms of UDR, PIP or object updates. Whole setup works correctly in such configuration
Caveats

## Slide 24: Active Passive
F(S) : Standard_F4 and above
Fsv2: Standard_F8(s)_v2 and above
Supported Azure VM sizes
https://docs.fortinet.com/vm/azure/fortigate/6.2/azure-cookbook/6.2.0/271726/instance-type-support
Notes: https://docs.fortinet.com/vm/azure/fortigate/6.2/azure-cookbook/6.2.0/271726/instance-type-support

## Slide 25: Active Passive with Azure Standard Load Balancer
Outbound (south - north):
  SNAT using external interface public IP if present or loadbalancer IP(‘s)
  Session is not recovering on FW failover
Inbound (north - south):
  DNAT by Azure from external Load Balancer interface public IP to private IP. Secondly DNAT using Virtual IP private IP to VM IP. If you select Floating IP in the load balancer you can use the public IP in the Virtual IP on the Fortigate
  SNAT not required. UDR send traffic back to the active unit
  Session is not recovering on FW failover
Internal (east – west):
  No NAT
  Session is not recovering on FW failover
Traffic flow

## Slide 26: Active Passive with Azure Standard Load Balancer
Site-2-Site VPN
  No NAT
  UDR routes for the client network needs to be routed back to the active firewall via internal Load Balancer
  IPSEC tunnel can be terminated on the public IP of external load balancer and terminated on the active firewall
  Upon failover the IPSEC VPN tunnel needs to reestablished to the passive firewall
Client-2-Site VPN
  No NAT
  UDR routes for the client network needs to be routed back to the active firewall
  VPN tunnel is terminated on the active firewall
Azure VPN Gateway - ExpressRoute
  No NAT
  UDR routes for the client network needs to be routed back to the active firewall via internal Load Balancer
Traffic flow

## Slide 27: Active Passive with Azure Standard Load Balancer
Fortinet documentation
  https://docs.fortinet.com/vm/azure/fortigate/6.2/azure-cookbook/6.2.0/651421/deploying-and-configuring-active-passive-ha
  https://docs.fortinet.com/vm/azure/fortigate/6.0/use-case-high-availability-for-fortigate-on-azure/6.0.0/651421/deploying-and-configuring-active-passive-ha
ARM Templates
  https://github.com/fortinetsolutions/Azure-Templates/tree/master/FortiGate/Active-Passive-HA-w-Azure-LBs
  https://github.com/jvhoof/fortinet-azure-solutions/tree/master/FortiGate/QuickStart-AP-ELB-ILB
  Click here to deploy: https://portal.azure.com/#create/Microsoft.Template/uri/https%3A%2F%2Fraw.githubusercontent.com%2Fjvhoof%2Ffortinet-azure-solutions%2Fmaster%2FFortiGate%2FQuickStart-AP-ELB-ILB%2Fazuredeploy.json
Microsoft:
  https://docs.microsoft.com/en-us/azure/architecture/reference-architectures/dmz/secure-vnet-hybrid
Resources

## Slide 28: Active Active with Standard Load Balancer

## Slide 29: Active Active with Azure Standard Load Balancer
Disadvantages
VPN
NAT behind each member
Virtual Network - VNET
Subnet External
Subnet Internal
Subnet backend 1
Subnet backend 2
Notes: No FGSP:
East-West
-south-west traffic (subnet 2 subnet) works without NAT enabled, it also works with SNAT but then you loose the information about original SRC IP
-when one of the HA machines is dead you loose your session and it is not reestablished
-new session can be established via Second Fortigate and Internal Load Balancer
-you can achieve microsegmentation between VMs if using UDR
-ICMP traffic between subnets is supported by ILB
South-North:
-traffic needs to use SNAT when going from internal subnet to Internet
-session is broken when Fortinet is dead, there is no session reconnection
-Azure Load Balancer does not support ICMP, only TCP & UDP are supported
-during Firewall failover you can establish new session via second Firewall with no problem
North-South (DSTNAT traffic)
-SNAT is mandatory in DST NAT Rule, you loose information about real IP in the backend system
-during failover of firewall session is lost. You can start new session via second working firewall
VPN traffic via Virtual Network Gateway
-Site 2 site traffic works both with SNAT enabled and diasbled. When you disable SNAT you need to configure UDR so Subnet Gateway knows how to reach your internal subnet for return traffic.
When configuring VPN you need to update UDR with information that the VPN peer network is available via ILB, on FW you need to add static route that peer VPN network is available via Azure Gateway on Port2. This static route might now work in GUI so you need to add it in CLI.
When using configuration synchronization with ‘config system auto-scale’ you need to be aware that settings are copied from Firwall A to B which can break your configuration. For example when using VIPs in DST NAT rules with external IP addresses those addresses are different on each box and copying them from firewall A to B will break the configuration. To solve the issue you can use the port and 0.0.0.0/0
Download of file via VPN tunnel:
During failover of FW wget keeps running in the background and after Firewall is back online wget session is continued and file is being downloaded despite the fact that DNAT SSH session was frozen during failover.

## Slide 30: Active Active with Azure Standard Load Balancer
North-south traffic inspection
East-west traffic inspection
ExpressRoute traffic inspection
Vertical scaling
Use cases

## Slide 31: Active Active with Azure Standard Load Balancer
Deployment requires a 2 NIC vm’s. A license supporting lower number of CPU’s can be used and will only use the number of CPU’s supported for the license
Failover time is defined by the failover detection of the Load Balancer. A probe fail time is 5 seconds and it has to fail 2 times. This results in a failover time of around 10-15 seconds
Failover causes sessions to block
MGMT is done by default over 2 public IP’s on the external side. This can be move to the internal side
Standard public IP’s require a NSG (Any, Any, Allow minimum) on each subnet or interface to function
SDN Fabric Connector can be used for dynamic address discovery
VPN Setup is complex each node needs to have an active tunnel and ECMP and/or dynamic routing.
Azure Load Balancer does not support ICMP, only TCP & UDP are supported
Caveats

## Slide 32: Active Active with Azure Standard Load Balancer
Configuration sync:
  No by default
  Autoscaling config sync: Syncing too much information. (Mantis 0537049)
  FortiManager: open bug not working in 6.0.4
Caveats
synctestfgt-A-18h02 (auto-scale) # show
config system auto-scale
set status enable
set role master
set sync-interface "port2"
set callback-url "${CALLBACK_URL}"
set psksecret <PSK>
end
synctestfgt-B (auto-scale) # show
config system auto-scale
set status enable
set sync-interface "port2"
set master-ip 10.0.2.5
set callback-url "${CALLBACK_URL}"
set psksecret <PSK>
end

## Slide 33: Active Active
F(S) : Standard_F1 and above
Fsv2: Standard_F1(s)_v2 and above
Supported Azure VM sizes
https://docs.fortinet.com/vm/azure/fortigate/6.2/azure-cookbook/6.2.0/271726/instance-type-support
Notes: https://docs.fortinet.com/vm/azure/fortigate/6.2/azure-cookbook/6.2.0/271726/instance-type-support

## Slide 34: Active Active with Azure Standard Load Balancer
Outbound (south - north): (TCP, UDP)
  SNAT using external interface public IP if present or loadbalancer IP(‘s)
  Session is not recovering on FW failover
  TCP & UDP
Inbound (north - south): (TCP, UDP)
  DNAT by Azure from external interface public IP to private IP. Secondly DNAT using Virtual IP private IP to VM IP. If you select Floating IP in the load balancer you can use the public IP in the Virtual IP on the Fortigate
  SNAT (visibility loss) or FGSP (sync session between cluster members) required
  TCP & UDP
  Session is not recovering on FW failover
Internal (east – west): (TCP, UDP, ICMP)
  No NAT required (LB uses a 5 tuple session state)
  Session is not recovering on FW failover
Traffic flow

## Slide 35: Active Active with Azure Standard Load Balancer
Site-2-Site VPN
  For VPN it is required that there is an active VPN tunnel to each of the nodes in the cluster
  SNAT (visibility loss) or FGSP (sync session between cluster members) required
Azure VPN Gateway - ExpressRoute
  No NAT
  UDR routes for the client network needs to be routed back to the active firewall
Traffic flow
Notes: As in the reference design from Microsoft it is advised to UDR route traffic from the an Azure Gateway (VPN and ExpressRoute) via the Internal Subnet Load Balancer. This will cause the sessions to be assigned to the same FGT node for back and forth traffic.
https://docs.microsoft.com/en-us/azure/load-balancer/load-balancer-distribution-mode
https://docs.microsoft.com/en-us/azure/load-balancer/load-balancer-ha-ports-overview

## Slide 36: Active Active with Azure Standard Load Balancer
Fortinet documentation
  https://docs.fortinet.com/vm/azure/fortigate/6.2/azure-cookbook/6.2.0/856171/deploying-and-configuring-azure-load-balancing-ha
  https://docs.fortinet.com/vm/azure/fortigate/6.0/use-case-high-availability-for-fortigate-on-azure/6.0.0/856171/deploying-and-configuring-azure-load-balancing-ha
ARM Templates
  https://github.com/fortinetsolutions/Azure-Templates/tree/master/FortiGate/Azure%20Active-Active%20LoadBalancer%20HA-Ports
  https://github.com/jvhoof/fortinet-azure-solutions/tree/master/FortiGate/QuickStart-AA-ELB-ILB
  Click here to deploy: https://portal.azure.com/#create/Microsoft.Template/uri/https%3A%2F%2Fraw.githubusercontent.com%2Fjvhoof%2Ffortinet-azure-solutions%2Fmaster%2FFortiGate%2FQuickStart-AA-ELB-ILB%2Fazuredeploy.json
Microsoft:
  https://docs.microsoft.com/en-us/azure/load-balancer/load-balancer-ha-ports-overview
Resources

## Slide 38: Active - Passive
ExpressRoute
On-Premise
Gateway Subnet
Virtual Network - VNET
Subnet 1
Subnet 2
Subnet 3
Azure Gateway
ExpressRoute
VPN
Routing table

## Slide 39: Active - Active
ExpressRoute
On-Premise
Gateway Subnet
Virtual Network - VNET
Subnet 1
Subnet 2
Subnet 3
Azure Gateway
ExpressRoute
VPN
Routing table

## Slide 40: Active/Passive setup with Basic SKU PIP
When you use BASIC SKU PIPs cluster works correctly:
  -with our without NSGs associated witn MGMT NIC4
  -with or without PIP attached to MGMT NIC4
  Failover time is ~3 minutes

## Slide 41: VNET Peering
Virtual Network - VNET
Subnet Protected A
Public IP
Subnet External
Subnet Internal
SubnetMgmt
Subnet HA Sync
172.16.136.0/26
172.16.136.64/26
172.16.136.128/26
172.16.136.192/26
172.16.137.0/24
10.0.0.0/16
.5
.6
.6
.5
.4
Public LB
Internal LB
Subnet Protected B
10.0.6.0/24
Subnet Spoke A
172.16.140/0/26
VNET Spoke 1 – 172.16.140.0/24
Subnet Spoke B
172.16.142.0/26
VNET Spoke 2 – 172.16.142.0/24

## Slide 42: VNET Peering
Virtual Network - VNET
Subnet Protected A
Public IP
Subnet External
Subnet Internal
SubnetMgmt
Subnet HA Sync
172.16.136.0/26
172.16.136.64/26
172.16.136.128/26
172.16.136.192/26
172.16.137.0/24
172.16.136.0/22
.5
.6
.6
.5
.4
Public LB
Internal LB
Subnet Protected B
172.16.138.0/24
Subnet Spoke A
172.16.140/0/26
VNET Spoke 1 – 172.16.140.0/24
Subnet Spoke B
172.16.142.0/26
VNET Spoke 2 – 172.16.142.0/24

## Slide 43
Azure Standard
Load Balancer
External – Public IP
FortiGate
Private IP
WebServer
Private IP
Azure Standard
Load Balancer
Internal - Private IP